## Slide 3
Webinar Notes
  Please use the Q & A utility to ask us any questions concerning
  the material being presented.
  Please contact Brittany Socha- chat line or email brittany.socha@arisafety.com if you would like a copy of the presentation.

## Slide 4: Leakage Current Testing 101 – Introduction
Shock Hazards
Potential shock hazards
Leakage Current
What is leakage current?
Touch Current
Examples
What is Touch Current?
Video demonstrations
Effects of current on the human body
Human body impedance
Types of insulation barriers
Touch current types
How it is measured
By the standards

## Slide 5: Potential Shock Hazards
Contact made from circuit point to ground
Contact made between two points of a circuit

## Slide 6: Effects of Electrical Current on the Human Body
These limits can vary between people and different environments. For example, women have a slightly different threshold then men for perception and pain as the result of exposure to electric current.

## Slide 7: Human Body Resistance
The human body on an average has about 1000 to 1500 ohms resistance.
The outer layer of the skin provides the largest percentage of the body’s electrical resistance.
The skin, has a breakdown voltage at which it ceases to act like a resistor and is simply “punctured” leaving only the lower resistance body tissue to impede the flow of current in the body.
The parts of the body which conduct the electricity the best are the blood vessels and nerves.

## Slide 8
I = 120V/1,000 Ohms = 0.120A
The current required to light a 7 watt, 120V lamp, passed across the chest is enough to cause fatality.

## Slide 9: Why Test?
The bottom line is that if you want to get your product to market and it can pose an electrical hazard, it has to be tested per various standards for approval.

## Slide 11
Poll Question 1

## Slide 12: Leakage Current

## Slide 13: Leakage Current
Leakage current is the stray current that actually flows on the surface of and through the insulation. It is undesired current that we want to quantify to better understand the quality of an insulation barrier.

## Slide 14: Leakage Current Types
1 – IEC 60990 2nd edition: Methods of Measurement of Touch Current and Protective Conductor Current
Touch Current
Electric current through a human body when it touches one or more accessible parts of an installation or of equipment1
Protective Conductor Current
Current which flows in a protective conductor1
Also called Earth Leakage Current.
Also called Enclosure Leakage Current.

## Slide 15: How is this Different?
A hipot test measures leakage through product insulation while the device is powered off. Insulation is stressed by high voltage and the resulting leakage current is measured.
Touch Current
Measured when the device is powered up during various operation states.
Hipot Leakage Current
Insulation stressed with high voltage and leakage current measured.

## Slide 16: How is it Measured?
Leakage current is measured by an MD under normal and single fault conditions. The main question to ask: What is the severity of electric current someone would be exposed to if they were to touch the DUT under such conditions?
MD
Leakage current is measured through a human body impedance network, also known as a Measuring Device (MD)
Body Impedance
MD is designed to simulate the impedance of the human body under various conditions.
Normal and Single Fault Conditions
Measurements taken under normal conditions.
Measurements also taken under single fault conditions to simulate worst case scenarios

## Slide 17: How is it Measured?
Medical Devices
IT Equipment
Electric Spas
MD will vary by product standard. Most MDs are derived from IEC 60990-1.

## Slide 18: Earth Leakage
MD will vary by product standard. Most MDs are derived from IEC 60990-1.

## Slide 19: Enclosure Leakage
MD will vary by product standard. Most MDs are derived from IEC 60990-1.

## Slide 28: By the Standards – IEC 60601-1 Medical Equipment

## Slide 29: By the Standards – IEC 61010-1 Laboratory Equipment

## Slide 30: By the Standards – IEC 60950 IT Equipment

## Slide 31
Poll Question 2

## Slide 33
Contact Us
If you would like a copy of this presentation please email Brittany Socha at brittany.socha@arisafety.com
Check out our website for more information arisafety.com

## Slide 34
JOIN US FOR OUR NEXT WEBINAR
Wednesday, October 11 10AM CT (GMT – 6:00) Leakage Current Testing -102
Click the link in chat box to learn more